## Slide 1: Utilizing Weather Station Data to Improve Crop Management
Daryl Herzmann
@akrherz
1 March 2018

## Slide 2: Why do weather stations exist?
PS. the Earth is not Flat.
Images: weather.gov
Planetary Boundary Layer
?????

## Slide 3: OK daryl, no more attempts at confusing drawings

## Slide 4: If Weather Stations are so important, why doesn’t the government place them like weeds over Iowa?
Money does not grow on trees
Maintaining weather stations is more expensive than installing them
Impractical to measure the variability that exists
  Caution: If variability scares you, avert your eyes for the next few slides

## Slide 5
ISU “Tall Towers” 1 second interval Wind Speed [mps]
Two sensors at same height, mounted at different directions on the tower. We also have 20 Hz data 
This entire plot is just 1 minute of data!

## Slide 6: Precipitation Variability
Iowa Flood Center experiment with tipping buckets 3 feet apart
Found some cases of noticeable differences between these two gauges
In general case, which gauge is right? 
http://iowafloodcenter.org/notes-from-the-field-rain-gauges/

## Slide 7: Temperature Variability
Subtle topography / elevation changes make a difference!
Similar to wind, one second plots sometimes show rapid temperature fluctuations
Urban Heat Islands impact temperature representativity
Photo: Dr Elywnn Taylor

## Slide 8: Bah, My weather station at my house is highly accurate!
https://www.wunderground.com/weatherstation/installationguide.asp

## Slide 9: OH daryl, LET US JUST GIVE Up and go have lunch!!!

## Slide 10: Having said all that, let us collect all the weather station data we can find!
Iowa Environmental Mesonet
“Meso” is a fancy weather term for a spatial scale (10s of miles)
Aggregate data from many different observation networks
Rest of my talk shamelessly promotes my website!

## Slide 11: Plugging my IEM Daily Feature
Highlights something hopefully relevant each day
RSS Feed if you don’t want to check website daily, also view past features
Often links to IEM app that generated the plot, so you can tweak, download raw data

## Slide 12
Select Plot Type
Select Plot Options
Description
Custom Generated Plot
Download Raw Data (Excel)
IEM Auto Plotting

## Slide 13: Which network should I use?
Data Need | Recommendation
“Daily” High/Low Temps + Precipitation | NWS COOP IEM “Long Term Climate” / “Climodat”
Wind | ISU Soil Moisture ASOS / AWOS (Airport weather stations)
Solar Radiation | ISU Soil Moisture
Hourly Rainfall, not snow | ISU Soil Moisture / ASOS / AWOS
River Stage | DCP (USGS gauges)
Soil Temperature/Moisture | ISU Soil Moisture / SCAN
Humidity | ISU Soil Moisture / ASOS / AWOS
Pavement Temperatures | RWIS
Unicorns | Sorry, we don’t have that, yet.

## Slide 14: How do I find my closest station within a given IEM network?
IEM -> Info Tab -> Station Data + Metadata

## Slide 15: Some Weather Variables to Monitor
Growing Degree Days
Temperatures
Soil Moisture/Temperature
Precipitation
Wind

## Slide 16: What are Growing Degree Days (GDD)?
Classic Equation for Corn
  Where:
  Daily hi/low is capped at 86F
  Daily hi/low is floored at 50F
  Base is 50F
Example 1
High 90
Low 48
GDD: (90 86 + 48 50)/2 – 50 = 18
Example 2
High 40
Low 32
GDD: (40 50 + 32 50)/2 – 50 = 0

## Slide 17
Web Link

## Slide 18
Web Link

## Slide 19
Web Link

## Slide 20
Web Link

## Slide 21: Some Weather Variables to Monitor
Growing Degree Days
Temperatures
Soil Moisture/Temperature
Precipitation
Wind

## Slide 22
Web Link

## Slide 23
Web Link (Autoplot #32)
2017 Daily Low Temp Departure
2016 Daily Low Temp Departure

## Slide 24
Web Link

## Slide 25
Web Link

## Slide 26: Some Weather Variables to Monitor
Growing Degree Days
Temperatures
Soil Moisture/Temperature
Precipitation
Wind

## Slide 27: ISU Soil Moisture Caveats Galore
Only 12, 24, and 50 inch depth readings for moisture
4 inch soil temperature is not in the crop field
Sensors don’t work properly when soil is frozen
We’ve had issues with lightning knocking out sensors
Newly installed sensors need time to find equilibrium

## Slide 28
Web Link

## Slide 29
Web Link (Autoplot #177)

## Slide 30
Web Link

## Slide 31: Some Weather Variables to Monitor
Growing Degree Days
Temperatures
Soil Moisture/Temperature
Precipitation
Wind

## Slide 32: What is an Arridity Index?
Normalize a departure by its Standard Deviation (units of sigma)
  Standard Deviation is a measure of the amount of spread/variability in the data
  For example, a 1 inch departure during the winter is different than summer
  Allows combination of temperature and precipitation with a common unit (sigma)
Equation (Std High Temperature) – (Std Precipitation)
Temperature | Precipitation | Arridity
Very Hot (2.5) | Wet (1) | 2.5 – 1 = 1.5
Warm (1) | Very Dry (-2.5) | 1 - -2.5 = 3.5
Cold (-1) | Wet (1) | -1 – 1 = -2
Very Cold (-2.5) | Very Dry (-2.5) | -2.5 - -2.5 = 0

## Slide 33
Web Link

## Slide 34
Web Link

## Slide 35
Web Link

## Slide 36
Web Link

## Slide 37: Some Weather Variables to Monitor
Growing Degree Days
Temperatures
Soil Moisture/Temperature
Precipitation
Wind

## Slide 38
Web Link

## Slide 39: February vs August Wind Rose
Web Link

## Slide 40: OK, enough of my rambling…. Questions? https://mesonet.agron.iastate.edu “Info” Tab -> Presentations
Twitter: @akrherz
akrherz@iastate.edu
515-451-9249